## Slide 1
Chapter 1: Computer Science Basics

## Slide 2
Learning Objectives
    Definition of Computer Architecture?
    What it means?
    What it involves?
    Importance?

## Slide 3
Computers are machines that perform calculations on data which can be used to do everything that we know and are able to express in logical and actionable items.
In theory every problem that can be expressed mathematically or logically can be solved using computers.
On a high level computer architecture defines the components of a computer system and their organization and responsibilities along with a set of instructions (ISA) that the computer understands.
Which means:
Computer Architecture: Definition
“In it’s broadest sense Computer Architecture defines the set of rules and guidelines that describe capabilities, structure and implementation of computer systems.”

## Slide 4
What It Involves?
Instruction Set Architecture
Microarchitecture
Logic Design
Hardware Implementation
04
03
02
01
Computer Architecture
Instruction Set Architecture
Hardware Implementation
Logic Design
Microarchitecture

## Slide 5
Instruction Set Architecture (ISA)
An instruction set architecture (ISA) is the interface between the computer's software and hardware and also can be viewed as the programmer's view of the machine.
A processor only understands instructions encoded in some numerical fashion, usually as binary numbers and a set of instructions that can be used to operate on those binary numbers.
Besides instructions, the ISA defines items in the computer that are available to a program—e.g. data types, registers, addressing modes, and memory. Instructions locate these available items with register indexes (or names) and memory addressing modes.

## Slide 6
Instruction Set Architecture (ISA)
Software
Hardware
Instruction Set

## Slide 7
Microarchitecture Design
Microarchitecture AKA computer organization is the way a given instruction set architecture (ISA) is implemented in a particular processor.
A specific ISA may be implemented with different microarchitectures, implementations may vary due to different goals of a given design or technology innovations.
Some of concepts related to the Microarchitecture Design are as follows:
  Instruction Cycle
  Instruction Set Choice
  Instruction Pipelining
  Cache
  Out-of-order execution
  Multiprocessing and Multithreading

## Slide 8
Microarchitecture Design
Execution Unit
Instruction Pipeline
Bus Interface Unit
System Bus
8086 Microarchitecture

## Slide 9
Logic Design
In electronics, logic synthesis is a process by which an abstract form of desired circuit behaviour, typically at register transfer level (RTL), is turned into a design implementation in terms of logic gates.
Register-Transfer Level (RTL) is a design abstraction which models a synchronous digital circuit in terms of the flow of digital signals (data) between hardware registers, and the logical operations performed on those signals.
Logic Gate is an idealized or physical device implementing a Boolean function; that is, it performs a logical operation on one or more logical inputs, and produces a single logical output. All logical values are Boolean values that represent either True or False.

## Slide 10
How are these logic functions actually computed in hardware?
Logic gates are constructed from transistors.
The output is a Boolean function of inputs.
The gate responds continuously to changes in input with a small delay.
Simple Boolean functions are implemented by “logic gates” which are more complex functions, by combinations of gates.

## Slide 11
Logic Design: Example
The diagram above is the hardware design for a simple 12-bit microprocessor.
The Simple-12 processor is a 12-bit single-cycle. The processor is designed to accept 12-bit instructions which are each composed of a 4-bit operation code and an 8-bit address.
Simple logic gates are used as the basis for the creation of more complex digital electronic circuits, as can be seen in the adjacent diagram, first we start with a layout for the overall system, then we add logical gates using transistors to build components to perform logical functions.
1
2
3
4
5
6
7

## Slide 12
Hardware Implementation
Hardware Implementation refers to the actual circuit design and devices that are used in implementation of a particular set of guidelines explained in the previous slide.
Hardware Implementation technology constraints:
  Restrict what can be done efficiently.
  New electronic technologies make new architecture implementation possible.
Hardware implementation is generally considered outside computer architecture because as electronics evolve the hardware might become efficient and the underlying architecture still remains the same.

## Slide 13
Modern Computer Systems

## Slide 14
Von Neumann Architecture
Von Neumann Architecture is a design architecture for an electronic digital computer with parts consisting of a processing unit containing an arithmetic logic unit and processor registers, a control unit containing an instruction register and program counter, a memory to store both data and instructions, external mass storage, and input and output mechanisms.
The meaning has evolved to be any stored-program computer in which an instruction fetch and a data operation cannot occur at the same time because they share a common bus.

## Slide 15
Components: Von Neumann machine

## Slide 16
Harvard Architecture

## Slide 17
Harvard Architecture vs Von Neumann Architecture
Von Neumann Architecture
Under pure Von Neumann Architecture the CPU can be either reading an instruction or reading/writing data from/to the memory.
Both cannot occur at the same time since the instructions and data use the same bus system.
Harvard Architecture
In a computer using the Harvard Architecture, the CPU can read an instruction and perform a data memory access at the same time, even without a cache.
A Harvard Architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway.
A Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight-bit byte that is not part of that twenty-four bit value.

## Slide 18
Modern Machines
All modern machines are modified Harvard architecture machines in the sense that they relax the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, which is a powerful technique). This modification is widespread in modern processors, such as the ARM architecture and x86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".
Another modification provides a pathway between the instruction memory (such as ROM or flash memory) and the CPU to allow words from the instruction memory to be treated as read-only data. This technique is used in some microcontrollers, including the Atmel AVR. This allows constant data, such as text strings or function tables, to be accessed without first having to be copied into data memory, preserving scarce (and power-hungry) data memory for read/write variables. Special machine language instructions are provided to read data from the instruction memory. (This is distinct from instructions which themselves embed constant data, although for individual constants the two mechanisms can substitute for each other.)

## Slide 19
Stored Program Concept
Stored-program concept is storage of instructions in computer memory to enable it to perform a variety of tasks in sequence or intermittently. The idea was introduced in the late 1940s by John von Neumann, who proposed that a program be electronically stored in binary-number format in a memory device so that instructions could be modified by the computer as determined by intermediate computational results.

## Slide 20
Advantages vs Disadvantages
Advantages of Stored Program Computers
Allows programs to be easily stored and loaded into the machine (processor) from the main memory.
Same set of control signal (s) for the instructions and data fetch.
Once a program has been developed and debugged, the numbers that represent its instructions can be written out onto a storage device, allowing the program to be loaded back into (main) memory at some point in the future.
Allows programs to treat themselves or other programs as data
Facilitates compilers, debuggers and programming tools designing.
Programs that treat themselves as data can also function as the self-modifying programs.
Disadvantages of Earlier Systems
Many computers were programmed.
Setting the switches or rewiring circuit boards to define the new program
Required a great deal of time
Prone to errors.
Suggested supplementary material:
https://youtu.be/ecIWPzGEbFc
https://youtu.be/sRAqEjbc6m8

## Slide 21
Stored Programs: Harvard Architecture

## Slide 22
Program Overview
For Programmer:
    Sequences of instructions that tell the computer what operations to do.
  E.g.: y = i * 4
For Processor:
    Program made up of a sequence of numbers that represent individual operations.
    These operations known as machine instructions or just instructions
  E.g.:
  Move bits from address of i into A register [A ≡ i]
  Allocate binary value of 4 into B register [B ≡ 4]
  Multiply A register * B register and put result in address denoted by y [y ≡ A*B]

## Slide 23
What are we learning in Next Chapter ?
    You will learn about Programming Languages
    We will learn about:
      History of programming language (it’s important too)
      Elements of a programming language
      Implementations of programming languages
      JIT and Runtimes/VMs
    We recommend the following for additional reading:
      https://en.wikipedia.org/wiki/Computer_architecture
      https://en.wikipedia.org/wiki/Von_Neumann_architecture
      https://en.wikipedia.org/wiki/Modified_Harvard_architecture
      http://infocenter.arm.com/help/topic/com.arm.doc.faqs/ka11516.html

## Slide 24: Thank You !